## Slide 1: THRILL WP 3.4
Udo Eisenbarth, Yannik Zobus

## Slide 2: Yet another optics simulation software ?
Proprietary licences
Not well-suited for large size laser systems (e.g. ghost focus calculation difficult)
Custom code hard / impossible to integrate
Existing solutions:
Our approach:
Open source
Platform for custom code integration
Extensible to specific needs
Model once – Use different analysis methods

## Slide 3: Simulation platform approach
Model arbitrary optical system as acyclic directed graphs
Software written in Rust (safety, modern, speed, memory efficient, inclusion of external code…)

## Slide 4: Simple setup (filter system)
Input energy: 1J
60/40 beam splitter
50% filter

## Slide 5: Simulating double-pass systems
Does not work!
(would form a loop)
Solution: „Reference nodes“
linked elements
(inverted)

## Slide 6: Example: Michaelson Interferometer

## Slide 7: Project status
Project plan
Optical model concept worked out
OPOSSUM v0.2.0
  technical concept preview (> 6000 lines of code)
  very basic command line interface (CLI)
  implementation of first simple nodes (source, detector, filter, beam splitter, etc..)
  implementation of group & reference nodes
  energy analyzer

## Slide 8: OPOSSUM ecosystem
  database for arbitrary material parameters
  db backend / web frontend architecture
  first preview version available
OpticDB
  database of standard optical elements
  in conception / planning
OPOSSUM Reporter
  generation of OPOSSUM analysis reports
  in conception / planning

## Slide 9: Outlook
planned milestones:
  v0.3: implementation of basic ray tracing (wavelength and polarization dependent)
  v0.4: inclusion of first external code (Python module: SHG simulation by M. Malki)